Conventional vs Solar Greenhouse Model Performance
Carl Chandler, PhD
Sun Aquasystems

The primary goal of the solar greenhouse model is to aid in developing better greenhouse designs. Designs that use less energy and are more productive should be more profitable, and model simulation should allow for optimization.

Below are are summaries of light, temperature, and heating demand for a conventional greenhouse and solar greenhouse of our own design.

south

Solar greenhouse Conventional greenhouse

The solar greenhouse has sub soil and north wall insulation, and R-40 (RSI-7) insulating blankets to cover glazing at night. Thermal storage in the north wall was not considered. The south wall is glazed as well as the south sloping 30 degree roof. South wall glazing area is equal to floor area, this ratio is the most important factor for increasing winter light availability.

The conventional greenhouse has negligible wall area, it is assumed it is very large and only roof glazing contributes. A 20 degree pitched roof with the ridge running from east to west is modelled. A typical commercial night energy curtain is used (R-1), sub soil is not insulated.

Both greenhouses use a double layer poly-EVA glazing with index of refraction 1.53 and IRAC film with 97% opacity to thermal infrared radiation.

Based on a simulation of 1 Jan 2007 to 15 Feb 2007:

monthly heating demand / m2 floor area solar greenhouse (kwh) = 1.13 monthly heating demand / m2 floor area conventional (kwh) = 23.92 monthly mean mol/m2 floor area day solar greenhouse = 14.78 monthly mean mol/m2 floor area day conventional = 5.04 mean daily temperature day solar greenhouse = 19.96 mean daily temperature day conventional= 18.71

Plots on following page.